## Slide 1: ECE 551 Digital Design And Synthesis
Fall ‘18
Lecture 2
  Verilog Syntax
  Structural Verilog
  Timing in Verilog

## Slide 2: Administrative Matters
Tutorial sessions
  Last section tonight 6:30 in B555
  Can also do on your own
If you are a windows user install ModelSim Student Edition.
OR…look at video on how to remote to Unix
Watch Videos on mid & final sections of Lecture02
  Quiz on these lectures next Monday in class.
Homework #1
  Due Next week by beginning of class

## Slide 3: Comments in Verilog
Commenting is important
  In industry many other poor schmucks are going to read your code
  Some poor schmuck (perhaps you 4 years later) are going to have to reference your code when a customer discovers a bug.
The best comments document why you are doing what you are doing, not what you are doing.
  Any moron who knows verilog can tell what the code is doing.
  Comment why (motivation/thought process) you are doing that thing.

## Slide 4: Commenting in Verilog
always @(posedge clk)
begin
Sig_FF1 <= Sig // Capture value of Sig Line in FF
Sig_FF2 <= Sig_FF1; // Flop Sig_FF1 to form Sig_FF2
Sig_FF3 <= Sig_FF2; // Flop Sig_FF2 to form Sig_FF3
end
// start_bit is ~Sig_FF2 & Sig_FF3
assign start_bit = (~Sig_FF2 && Sig_FF3) ? 1’b1 : 1’b0;
(Read with sarcasm)
“Thanks for the commenting the code pal. It tells me so much more than the verilog itself”.

## Slide 5: Commenting in Verilog
always @(posedge clk)
/********************************************
* Sig is asynchronous and has to be double flopped *
* for meta-stability reasons prior to use ************
*********************************/
begin
Sig_FF1 <= Sig;
Sig_FF2 <= Sig_FF1; // double flopped meta-stability free
Sig_FF3 <= Sig_FF2; // flop again for use in edge detection
end
/**********************************************
* Start bit in protocol initiated by falling edge of Sig line *
**********************************************/
assign start_bit = (~Sig_FF2 && Sig_FF3) ? 1’b1 : 1’b0;
This is better commenting. It tells you why stuff was done
Can see 2 types
of comments.
Comment to end of line is //
Multi line comment starts with /* and ends with */

## Slide 6: Numbers in Verilog
General format is: <size>’<base><number>
Examples:
  4’b1101 // this is a 4-bit binary number equal to 13
  10’h2e7 // this is a 10-bit wide number specified in hex
Available bases:
  d = decimal (please only use in test benches)
  h = hex (use this frequently)
  b = binary (use this frequently for smaller #’s)
  o = octal (who thinks in octal?, please avoid)

## Slide 7: Numbers in Verilog
Numbers can have x or z characters as values
  x = unknown, z = High Impedance
  12’h13x // 12-bit number with lower 4-bits unknown
If size is not specified then it depends on simulator/machine.
  Always size the number for the DUT verilog
    Why create 32-bit register if you only need 5 bits?
    May cause compilation errors on some compilers
Supports negative numbers as well
  -16’h3A // this would be -3A in hex (i.e. FFC6 in 2’s complement)
  I rarely if ever use this. I prefer to work 2’s complement directly

## Slide 8: Identifiers (Signal Names)
Identifiers are the names you choose for your signals
In a programming language you should choose descriptive variable names. In a HDL you should choose descriptive signal names.
  Use mixed case and/or _ to delimit descriptive names.
    assign parityErr = ^serial_reg;
    nxtState = returnRegister;
  Have a convention for signals that are active low
    Many errors occur on the interface between blocks written by 2 different people. One assumed a signal was active low, and the other assumed it was active high
    I use _n at the end of a signal to indicate active low
    rst_n = 1’b0 // assert reset

## Slide 9: Signal Values & Strength in Verilog
Signals can have 1 of 4 values
Value: | Meaning:
0 | Logic zero, false condition
1 | Logic one, true condition
x | Unknown, either uninitialized or in contention
z | High impedance. Not driven, or not connected
Need high impedance for modeling of tri-state
busses
16
16
EEPROM
RAM
16
16
rd_ram
rd_eep
CPU
dbus[15:0]
clk
q
What value
does q have prior to any positive clock edge?
d
It is unknown: x
(uninitialized)

## Slide 10
Resolving 4-Value Logic
A
B
OUT
A B OUT
0 0 0
0 1 1
1 1 1
0 x
0 z
1 x
1 z
A B OUT
0 0 0
0 1 0
1 1 1
0 x
0 z
1 x
1 z
A
B
OUT
A
B
OUT
S A T B OUT
0 0 z z
0 1 z x
0 x z 1
0 z z 0
1 0 0 1
1 0 0 z
1 1 1 z
1 x x z
1 z x 0
S
T
A
OUT
A
OUT
0 1 x z
1 0 x
X
X
X
1
1
0
0
x
x
z
x
1
0
x
0
1
x
x

## Slide 11
Signal Values & Strength in Verilog
Strength Level | Meaning:
supply | Strongest (like a supply VDD or VSS)
strong | Strong (default if not specified)
pull | Medium strength (like a pullup device)
weak | Weak, like a keeper (sustainer, leaker)
highz | High impedance
Concept of drive strength supported to model certain CMOS circuits that utilize contention.
D
Q
E
inv1
inv2
not inv1 (Q,n1)
not (weak0,weak1) inv2 (n1,Q)

## Slide 12: Registers in Verilog
Registers are storage nodes
  They retain their value till a new value is assigned
  Unlike a net (wire) they do not need a driver
  Can be changed in simulation by assigning a new value
Registers are not necessarily FlipFlops
  In your DUT Verilog registers are typically FlipFlops
  Anything assigned in an always or initial block must be assigned to a register
  You will use registers in your testbenches, but they will not be FlipFlops

## Slide 13: Vectors in Verilog
Vectors are a collection of bits (i.e. 16-bit wide bus)
////////////////////////////////////////////////////////////////////
// Define the 16-bit busses going in and out of the ALU //
//////////////////////////////////////////////////////////////////
wire [15:0] src1_bus,src2_bus,dst_bus;
///////////////////////////////////////////////////////////////
// State machine has 8 states, need a 3-bit encoding //
/////////////////////////////////////////////////////////////
reg [2:0] state,nxt_state;
Bus ≠ Vector (how are they different?)

## Slide 14: Vectors in Verilog
Can select parts of a vector (single bit or a range)
left shift
src
result
16
16
shft_in
shft_out
module lft_shift(src,shft_in,result,shft_out);
input [15:0] src;
input shft_in;
output [15:0] result;
output shft_out;
/////////////////////////////////////////////////////////////////////////
// Can access 15 LSB’s of src with [14:0] selector //
// { , } is a process of concatenating two vectors to form one //
//////////////////////////////////////////////////////////////////////
assign result = {src[14:0],shft_in};
assign shft_out = src[15]; // can access a single bit MSB with [15]
endmodule

## Slide 15: Arrays & Memories
Can have multi-dimentional arrays
  reg [7:0] mem[0:99][0:3]; // what is this?
Often have to model memories
  RF, SRAM, ROM, Flash, Cache
  Memories can be useful in your test bench
wire [15:0] src1,src2; // source busses to ALU
reg [15:0] reg_file[0:31]; // Register file of 32 16-bit words
reg [4:0] addr1,addr2; // src1 and src2 address
.
.
.
src1 = reg_file[addr1]; // transfer addressed register file
// to src1 bus
ALU
RF
Flash
I2C
result
addr1
addr2
src1
src2

## Slide 16: Parameters & Define
Parameters are useful to make your code more generic/flexible. More later…
`define statement can make code more readable
`define idle = 2’b00; // idle state of state machine
`define conv = 2’b01; // in this state while A2D converting
`define avg = 2’b10; // in this state while averaging samples
.
.
.
case (state)
`idle : if (start_conv) nxt_state = `conv;
else nxt_state = `idle
`conv : if (gt) nxt_state = `avg;
else nxt_state = `conv;
.
.
.
Bad Example…Don’t Use `define for state assignment
Use localparam instead. `define should be truly global thing

## Slide 17: Parameters & Define
localparam idle = 2’b00; // idle state of state machine
localparam conv = 2’b01; // in this state while A2D converting
localparam accum = 2’b10; // in this state while averaging samples
.
.
.
case (state)
idle : if (start_conv) nxt_state = conv;
else nxt_state = idle
conv : if (gt) nxt_state = avg;
else nxt_state = conv;
.
.
.
Read Cumming’s paper on use of define & param. Posted on web under “reference”

## Slide 18: System Verilog…Better Yet
System verilog adds an enumerated type.
typedef enum reg [1:0] { IDLE, CONV, ACCM } state_t;
state_t state, nxt_state; // declare state and nxt_state signals
case (state)
IDLE : if (strt_cnv) begin
clr_dac = 1;
clr_smpl = 1;
nxt_state = CONV;
end
CONV : if (!gt) begin
inc_dac = 1;
nxt_state = CONV;
  . . .
state
IDLE
CONV
ACCM
CONV
Makes debug much easier

## Slide 19: Useful System Tasks
$display  Like printf in C. Useful for testbenches and debug
$display(“At time %t count = %h”,$time,cnt);
$stop  Stops simulation and allows you to still probe signals and debug
$finish  completely stops simulation, simulator relinquishes control of thread.
Also useful is `include for including code from another file (like a header file)
Read about these features of verilog in your text

## Slide 20: Full Adder: Structural
module half_add (X, Y, S, C);
input X, Y ;
output S, C ;
xor SUM (S, X, Y);
and CARRY (C, X, Y);
endmodule
module full_add (A, B, CI, S, CO) ;
input A, B, CI ;
output S, CO ;
wire S1, C1, C2;
// build full adder from 2 half-adders
half_add PARTSUM (A, B, S1, C1),
SUM (S1, CI, S, C2);
// … add an OR gate for the carry
or CARRY (CO, C2, C1);
endmodule

## Slide 21: Full Adder: RTL/Dataflow
module fa_rtl (A, B, CI, S, CO) ;
input A, B, CI ;
output S, CO ;
// use continuous assignments
assign S = A ^ B ^ CI;
assign C0 = (A & B) | (A & CI) | (B & CI);
endmodule
Data flow Verilog is
often very concise
and still easy to read
Works great for most
boolean and even
datapath descriptions

## Slide 22: Full Adder: Behavioral
Circuit “reacts” to given events (for simulation)
  Actually list of signal changes that affect output
module fa_bhv (A, B, CI, S, CO) ;
input A, B, CI;
output S, CO;
reg S, CO; // assignment made in an always block
// must be made to registers
// use procedural assignments
always@(A or B or CI)
begin
S = A ^ B ^ CI;
CO = (A & B) | (A & CI) | (B & CI);
end
endmodule

## Slide 23: Full Adder: Behavioral
IN SIMULATION
  When A, B, or C change, S and CO are recalculated
IN REALITY
  Combinational logic – no “waiting” for the trigger
  Constantly computing - think transistors and gates!
  Same hardware created for all three types of verilog
always@(A or B or CI)
begin
S = A ^ B ^ CI;
CO = (A & B) | (A & CI) | (B & CI);
end
majority
S
CO
A
B
CI
fa_bhv

## Slide 24: Structural Basics: Primitives
Build design up from the gate/flip-flop/latch level
  Structural verilog is a netlist of blocks and connectivity
Verilog provides a set of gate primitives
  and, nand, or, nor, xor, xnor, not, buf, bufif1, etc.
  Combinational building blocks for structural design
  Known “behavior”
  Cannot access “inside” description
Can also model at the transistor level
  Most people don’t, we won’t

## Slide 25: Primitives
No declarations - can only be instantiated
Output port appears before input ports
Optionally specify: instance name and/or delay (discuss delay later)
and N25 (Z, A, B, C); // name specified
and #10 (Z, A, B, X),
(X, C, D, E); // delay specified, 2 gates
and #10 N30 (Z, A, B); // name and delay specified

## Slide 26: Syntax For Structural Verilog
First declare the interface to the module
  Module keyword, module name
  Port names/types/sizes
Next, declare any internal wires using “wire”
  wire [3:0] partialsum;
Then instantiate the primitives/submodules
  Indicate which signal is on which port
ModelSim Example with ring oscillator

## Slide 27: Hierarchy
Any Verilog design you do will be a module
This includes testbenches!
Interface (“black box” representation)
  Module name, ports
Definition
  Describe functionality of the block
Instantiation
  Use the module inside another module

## Slide 28: Hierarchy
Build up a module from smaller pieces
  Primitives
  Other modules (which may contain other modules)
Architecture: typically top-down
Design & Verification: typically bottom-up
Add_full
Add_half
or
Add_half
and
xor
and
xor
Full Adder Hierarchy

## Slide 29: Add_half Module
module Add_half(c_out, sum, a, b);
output sum, c_out;
input a, b;
xor sum_bit(sum, a, b);
and carry_bit(c_out, a, b);
endmodule
Add_half
and
xor

## Slide 30: Add_full Module
module Add_full(c_out, sum, a, b, c_in) ;
output sum, c_out;
input a, b, c_in;
wire w1, w2, w3;
Add_half AH1(.sum(w1), .c_out(w2), .a(a), .b(b));
Add_half AH2(.sum(sum), .c_out(w3), .a(c_in), .b(w1));
or carry_bit(c_out, w2, w3);
endmodule
Add_full
Add_half
or
Add_half

## Slide 31: Can Mix Styles In Hierarchy!
module Add_half_bhv(c_out, sum, a, b);
output reg sum, c_out;
input a, b;
always @(a, b) begin
sum = a ^ b;
c_out = a & b;
end
endmodule
module Add_full_mix(c_out, sum, a, b, c_in) ;
output sum, c_out;
input a, b, c_in;
wire w1, w2, w3;
Add_half_bhv AH1(.sum(w1), .c_out(w2),
.a(a), .b(b));
Add_half_bhv AH2(.sum(sum), .c_out(w3),
.a(c_in), .b(w1));
assign c_out = w2 | w3;
endmodule

## Slide 32: Hierarchy And Scope
Parent cannot access “internal” signals of child
If you need a signal, must make a port!
Example: Detecting overflow Overflow = cout XOR cout6 Must output overflow or cout6!
module add8bit(cout, sum, a, b, cin);
output [7:0] sum;
output cout;
input [7:0] a, b,cin;
wire cout0, cout1,… cout6;
FA A0(cout0, sum[0], a[0], b[0], cin);
FA A1(cout1, sum[1], a[1], b[1], cout0);
…
FA A7(cout, sum[7], a[7], b[7], cout6);
endmodule

## Slide 33: Hierarchy And Source Code
Can have all modules in a single file
  Module order doesn’t matter!
  Good for small designs
  Not so good for bigger ones
  Not so good for module reuse (cut & paste)
Can break up modules into multiple files
  Helps with organization
  Lets you find a specific module easily
  Good for module reuse (add file to project)

## Slide 34: Structural Verilog: Connections
Positional or Connect by reference
  Can be okay in some situations
    Designs with very few ports
    Interchangeable input ports (and/or/xor gate inputs)
  Gets confusing for large #s of ports
wire [1:0] X;
wire W_n;
wire [3:0] word;
// instantiate decoder
dec_2_4_en DX (X, W_n, word);
module dec_2_4_en (A, E_n, D);
input [1:0] A;
input E_n;
output [3:0] D;
.
.
.
Partial code instatiating decoder

## Slide 35: Structural Verilog: Connections
Explicit or Connect by name method
  Helps avoid “misconnections”
  Don’t have to remember port order
  Can be easier to read
  .<port name>(<signal name>)
module dec_2_4_en (A, E_n, D);
input [1:0] A;
input E_n;
output [3:0] D;
  .
  .
  .
wire [1:0] X;
wire W_n;
wire [3:0] word;
// instantiate decoder
dec_2_4_en DX (.A(X), .E_n(W_n), .D(word));
Partial code instatiating decoder

## Slide 36: Empty Port Connections
Example: module dec_2_4_en(A, E_n, D);
  dec_2_4_en DX (.A(X), .D(word)); // E_n is high impedence
  dec_2_4_en DX (.A(X), .E_n(W_n) , ); // Outputs D[3:0] unused.
General rules
  Empty input ports => high impedance state (z)
  Empty output ports => output not used
Specify all input ports anyway!
  Z as an input is very bad…why?
Helps if no connection to output port name but leave empty:
  dec_2_4_en DX(.A(X[3:2]), .E_n(W_n), .D());

## Slide 37: Module Port List
Multiple ways to declare the ports of a module
module Add_half(c_out, sum, a, b);
output sum, c_out;
input a, b;
…
endmodule
module Add_half(output c_out, sum,
input a, b);
…
endmodule

## Slide 38: Module Port List
Multiple ways to declare the ports of a module (example2)
module xor_8bit(out, a, b);
output [7:0] out;
input [7:0] a, b;
…
endmodule
module xor_8bit(output [7:0] out, input [7:0] a, b);
…
endmodule

## Slide 39: Why Know Structural Verilog?
Code you write to be synthesized will almost all be dataflow or behavioral
You will write your test bench primarily in behavioral
What needs structural Verilog?
  Building hierarchy (instantiating blocks to form higher level functional blocks)
  There are somethings you can’t trust to synthesis, and need to instantiate library gates structurally and use `don’t touch directives for synthesis.
    Intentional clock gating
    Cross coupled SR latches
  Synthesis tools output structural verilog (gate level netlist). You need to be able to read this output.

## Slide 40
Timing Controls For Simulation
Can put “delays” in a Verilog design
  Gates, wires, & behavioral statements
Delays are useful for Simulation only!
  Used to approximate “real” operation while simulating
  Used to control testbench
SYNTHESIS
  Synthesis tool IGNORES these timing controls
    Cannot tell a gate to wait 1.5 nanoseconds
    Delay is a result of physical properties
  Only timing (easily) controlled is on clock-cycle basis
    Can tell synthesizer to attempt to meet cycle-time restriction

## Slide 41: Zero Delay vs. Unit Delay
When no timing controls specified: zero delay
  Unrealistic – even electrons take time to move
  OUT is updated same time A and/or B change: and A0(OUT, A, B)
Unit delay often used
  Not accurate either, but closer…
  “Depth” of circuit does affect speed!
  Easier to see how changes propagate through circuit
  OUT is updated 1 “unit” after A and/or B change: and #1 A0(OUT, A, B);

## Slide 42: Zero/Unit Delay Example
A
B
C
Z
T A B C Y Z
T A B C Y Z
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
0 0 0 0 0
0 0 1 0 0
0 1 0 0 0
0 1 1 1 1
1 0 0 0 1
1 0 1 0 1
1 1 0 0 1
1 1 1 1 1
0 0 0 0 0
0 0 1 0 0
0 1 0 0 0
0 1 1 1 1
1 0 0 0 1
1 0 1 0 1
1 1 0 0 1
1 1 1 0 1
0 1 0 x x
0 1 0 0 x
0 1 0 0 0
0 1 1 0 0
0 1 1 1 0
0 1 1 1 1
1 0 0 1 1
1 0 0 0 1
1 1 1 0 1
1 1 1 1 1
1 0 0 1 1
1 0 0 0 1
0 1 0 0 1
0 1 0 0 0
0 1 1 0 0
0 1 1 1 0
0 1 1 1 1
Y
Zero Delay
Unit Delay
Zero Delay:
Y and Z change at same “time” as A, B, and C!
Unit Delay:
Y changes 1 unit after B, C
Unit Delay:
Z changes 1 unit after A, Y

## Slide 43: Types Of Delays
Inertial Delay (Gates)
  Suppresses pulses shorter than delay amount
  In reality, gates need to have inputs held a certain time before output is accurate
  This models that behavior
Transport Delay (Nets)
  “Time of flight” from source to sink
  Short pulses transmitted
Not critical for our project, however, in industry
  After APR an SDF is applied for accurate simulation
  Then corner simulations are run to ensure design robust

## Slide 44: Delay Examples
wire #5 net_1; // 5 unit transport delay
and #4 (z_out, x_in, y_in); // 4 unit inertial delay
assign #3 z_out = a & b; // 3 unit inertial delay
wire #2 z_out; // 2 unit transport delay
and #3 (z_out, x_in, y_in); // 3 for gate, 2 for wire
wire #3 c; // 3 unit transport delay
assign #5 c = a & b; // 5 for assign, 3 for wire

## Slide 45: Combinational Logic will Generate Pulses
clk
Have 3 Flops with a unit delay clk2q
Feeds simple combinational logic with unit gate delays
11
10
01
A,B,C make the transitions shown
What does “out” do?
A
B
C
n1
1
1
out
clk
A
B
C
n1
out

## Slide 46: Inertial Delay (tries to model gate delay)
clk
11
10
01
A
B
C
n1
1
1
out
2
If we add a buffer with a 2 unit delay to the end of this circuit, now what happens?
Remember the inertial gate delay will filter any pulse shorter than the specified delay…The pulse is eaten.

## Slide 47: Gate Delay Variation (Verilog Handles This)
Gates don’t have same delay in a rising transition vs falling
A
B
Z
NOR Gate:
Slow on rise
Fast on fall
A
B
Z
NAND3 Gate:
Roughly equal
Rise/fall
C
Gates delays are not constant
  Vary with PVT (Process, Voltage, Temperature)
  You will hear reference to PVT corners
    (fff,typ,sss) = (min,typ,max)

## Slide 48: Rise/Fall/Turn Off
in
out
in
out
Trise
in
out
Tfall
Referenced to
what the output
of the gate is doing
not #(2,1) inv1(out,in); // not gate with 2 unit rise and 1 unit fall
in
out
en
in
en
out
Z
HiZ
Toff
bufif1 #(1,1,2) tri1(out,in,en); // tri-state gate with unit rise/fall and 2 unit off
Turn Off delay =
Time from cntrl to high impedance

## Slide 49: Min/Typ/Max Delay
Speed, Speed, Speed ….
  If you need to ensure speed of your circuit you want to perform your worst case analysis with the longest (max) delays.
Perhaps more dangerous is a min-delay case. Race condition. If circuit has a race that is not met, it will fail at any clock speed.
  To ensure your circuit is immune to race conditions (i.e. clock skew) you want to perform your worst case analysis with shortest (min) delays.

## Slide 50: Min/Typ/Max
Verilog supports different timing sets.
and #(1:2:3) g1(out,a,b); // 1 ns min, 2ns typical, 3ns max delay
Can specify min/typ/max for rise and fall separate)
and #(2:3:4, 1:2:3) g1(out,a,b); // gate has different rise,fall for min:typ:max
Selection of timing set can is typically done in simulation environment
% verilog test.v +maxdelays
Invoke command line verilog engine
(like Verilog XL) selecting the maxdelay time set.

## Slide 51: Design Flow
DUT Verilog
Code
Verilog
Simulator
Verilog
Testbenches
Bugs?
Synthesis
Yes
Yes
Gate Level
Struct .v
Modified
Testbenches
Verilog
Simulator
Bugs?
Yes
Yes
Synth
script
APR
layout
SDF Files
Finally one has to
simulate gate level
again using SDF Files