## Slide 1: ECE 551 Digital System Design & Synthesis
Synthesis

## Slide 2: Administrative Matters
Team Formation (teams of 3-4)
  Start arranging your teams
Midterm is Monday Mar. 11th in EH1800
HW3 Due Wednesday 6th@ Class

## Slide 3: Synthesis Priorities
First there is functionality
  Is function coded in Verilog same as synthesized netlist?
    Boolean correct
    Sequential correct
    No uninteded latches or strange clock gating
Next there are design rules
  Is the fanout reasonable.
  Are my transition times fast enough (Hot Electron)
Finally there are performance criteria
  Speed
  Power
  Area

## Slide 4: Synthesis is cost function driven
Cost is a function of:
  Timing
  Area
  Power
In this priority order
Cost(mapping) = -Slack(mapping) +
Area(mapping) +
[power(mapping)]
Explore mapping space to minimize
this function (not the exact function)
Mapping refers to the mapping of the logic (elaborated database) to the cell library
Synopsys is a bit like the typical ECE Student…Smart, but a touch lazy
  Loose Constraints  Loose Design

## Slide 5: What Needs Constraint?
Combinational
Combinational
Combinational
clk
primary
inputs
primary
outputs
input to D
delays
Q to output
delays
clk
cycle time
input delay
output delay

## Slide 6: Setting Basic Timing Constraints
Establishing clock period, waveform, and pin it is sourced to:
create_clock -name "clk" -period 20 -waveform { 0 10 } clk
Name of clock, (a handle) not the pin it is sourced to
Pin this clock is sourced to
rise @ 0ns
fall @ 10ns
period = 20ns
Clock is no ordinary input. Can’t let Synopsys buffer it and do other silly such things.
If clock distribution requires buffering then that will be done by a separate tool (CTS) inside the APR environment.

## Slide 7: Defining Input Delay
clk
input delay
Combinational
source
of input
to DUT
clk
Combinational
clk
input delay is specified as time after the clock edge (of prior clock cycle)
that the input to the DUT is valid.
DUT
t – input_delay

## Slide 8: Defining Output Delay
clk
output delay
Combinational
clk
Combinational
clk
output delay is specified as time prior to next rising edge that the output has to be valid.
DUT
t – output_delay

## Slide 9: What Else Needs Constraint?
in
out
tPHL
in
out
in
out
tPHL
Propagation delay of a gate is not constant
  There is a term that depends on input slope
  Synthesis knows the capacitance of a primary input
  Synthesis does not know the drive strength of a primary input
We must inform Synopsys about the drive strength of the inputs
  set_driving_cell -lib_cell <cell> -pin Z -library <lib> <list_of_inputs>
  set_drive <# of ohms> <signal>

## Slide 10: What Else Needs Constraint?
in
out
tPHL
in
out
in
out
tPHL
Capacitive loading affects the propagation delay of a gate
  For a given drive strength the slope of the output will elongate with increased capacitive load
  Synopsys needs to know the capacitive load of primary outputs so it can size gates (or buffer up) to drive load with “crisp” transition times.
We must inform Synopsys about the load on primary outputs
  set_load <capacitance> <list of outputs>
Small
load
in
out
Big
load

## Slide 11: Anything More Need Constraints?
in
parasitic
??pF
What is the parasitic capacitance of this node?
  gate capacitance is known by Synopsys
  routing capacitance is the unknown
  how to estimate?
    fanout
    size of design (gate count)
set_wire_load_model -name <m_name> -library <lib_name>

## Slide 12: Are We Done Yet…Not Quite
n+
n+
2.0V
2.0V
p-substrate
VDS
IDS
VGS=1.0
VGS=1.5
VGS=2.0
When both VDS and VGS are high a transistor is conducting heavily.
Electrons “flying” across the channel get a lot of kinetic energy.
These electrons are also attracted to the surface by the high gate potential.
They can embed themselves in the gate oxide (causes VT degradation).
This is called “Hot Electron Effect”
Need to limit operating time at high VDS & VGS. Need “snappy” transitions.
set_max_transition_time <time> [current_design]

## Slide 13: GUI’s are for Children
GUI’s are for learning and some instances of debugging.
Once you know the tool you will mainly work in shell mode (at least that is my preference):
  unix_prompt>design_vision –shell dc_shell

## Slide 14: Sample DC Shell Script [1]
read_file -format verilog {./source/ss_a2d_dp.v}
###########################
# Define clock and set don't mess with it #
##########################
create_clock -name "clk" -period 20 -waveform { 0 10 } { clk }
set_dont_touch_network [find port clk]
# setup pointer that contains all inputs except clock #
set prim_inputs [remove_from_collection [all_inputs] [find port clk]]
#########################
# Set input delay & drive on all inputs #
########################
set_input_delay -clock clk 5 [copy_collection $prim_inputs]
set_driving_cell -lib_cell AO33D0BWP -pin Z -from_pin A1 -library \
tcbn40lpbwptc [copy_collection $prim_inputs]
# tell it por_n strongly driven so it won't buffer
set_drive 0.1 por_n

## Slide 15: Sample DC Shell Script [2]
##########################
# Set output delay & load on all outputs #
##########################
set_output_delay -clock clk 5 [all_outputs]
set_load 0.10 [all_outputs]
#####################################
# Wire load model allows it to estimate internal parasitics #
####################################
set_wire_load_model -name TSMC32K_Lowk_Conservative \
-library tcbn40lpbwptc
##################################
# Max transition time is important for Hot-E reasons #
#################################
set_max_transition 0.10 [current_design]
#########################
# Now actually synthesize for 1st time #
#########################
compile -map_effort low

## Slide 16: Sample DC Shell Script [3]
check_design
## design ware component caused extra pins
report_area
########################
# Take a look at max & min timings #
#######################
report_timing -path full -delay max -nworst 3
report_timing -path full -delay min -nworst 3
## smash the hierarchy (design ware component)
ungroup –all
compile -map_effort medium
check_design
report_area
#### write out final netlist ######
write –format verilog ss_a2d_dp –output ss_a2d_dp.vg
Now lets run this line by line and
see what it does

## Slide 17: Some “Nice to Have” Constraints
set_max_area 20000
  Sets maximum area to 20,000 area units (square microns)
set_max_dynamic_power 10
  Sets maximum dynamic power to 10 mW (default unit for our library is mW)
Note: Power & Speed often work against each other.
  A tight timing constrained design will use more parallel hardware.
  More nodes toggling, results computed and then discarded
Note: Area & Power often work together.
  In general less area => less toggling nodes
  less net capacitance switching

## Slide 18: Timing Reports….How do I read these?
dc_shell-xg-t> report_timing -delay max –nworst 1
****************************************
Report : timing
-path full
-delay max
-max_paths 1
Design : ss_a2d_dp
Version: Y-2006.06-SP1
Date : Thu Oct 2 09:00:42 2008
****************************************
Operating Conditions: NOM Library: gflxp
Wire Load Model Mode: enclosed
Startpoint: DAC_reg[0] (rising edge-triggered flip-flop clocked by clk)
Endpoint: DAC_full (output port clocked by clk)
Path Group: clk
Path Type: max
Report continued next page
report the worst timing path for max delay scenario
Startpoint <signal> <type>
Endpoint <signal> <type>
Very useful to look at

## Slide 19: Timing Reports….How do I read these?
Point Incr Path
-----------------------------------------------------------
clock clk (rise edge) 0.00 0.00
clock network delay (ideal) 0.00 0.00
DAC_reg[0]/CP (FD2LQM3P) 0.00 0.00 r
DAC_reg[0]/Q (FD2LQM3P) 0.25 0.25 r
U59/Z (AND3M1P) 0.10 0.35 r
U55/Z (ND4M2P) 0.13 0.48 f
U56/Z (NR3M6P) 0.21 0.69 r
DAC_full (out) 0.00 0.69 r
data arrival time 0.69
clock clk (rise edge) 20.00 20.00
clock network delay (ideal) 0.00 20.00
output external delay -5.00 15.00
data required time 15.00
-----------------------------------------------------------
data required time 15.00
data arrival time -0.69
-----------------------------------------------------------
slack (MET) 14.31
+ slack is a good thing, it means met timing

## Slide 20: Timing Report…min delay
dc_shell-xg-t> report_timing -delay min -nworst 1
Information: Updating design information... (UID-85)
****************************************
Report : timing
-path full
-delay min
-max_paths 1
Design : ss_a2d_dp
Version: Y-2006.06-SP1
Date : Thu Oct 2 09:17:50 2008
****************************************
Operating Conditions: NOM Library: gflxp
Wire Load Model Mode: enclosed
Startpoint: accum_reg_reg[0]
(rising edge-triggered flip-flop clocked by clk)
Endpoint: accum_reg_reg[0]
(rising edge-triggered flip-flop clocked by clk)
Use keywork min to get this report
Surprise, Surprise, the min delay is a path between two flops
Report continued next page

## Slide 21: Timing Report…min delay
Point Incr Path
-----------------------------------------------------------
clock clk (rise edge) 0.00 0.00
clock network delay (ideal) 0.00 0.00
accum_reg_reg[0]/CP (FD2LQM1P) 0.00 0.00 r
accum_reg_reg[0]/Q (FD2LQM1P) 0.11 0.11 f
U67/Z (EOFM1P) 0.05 0.16 r
accum_reg_reg[0]/D (FD2LQM1P) 0.00 0.16 r
data arrival time 0.16
clock clk (rise edge) 0.00 0.00
clock network delay (ideal) 0.00 0.00
accum_reg_reg[0]/CP (FD2LQM1P) 0.00 0.00 r
library hold time 0.08 0.08
data required time 0.08
-----------------------------------------------------------
data required time 0.08
data arrival time -0.16
-----------------------------------------------------------
slack (MET) 0.09
Oh good, we made it

## Slide 22: Hold time (worst case is back to back FF’s)
clk
clk
Tclk2q=0.11ns
Thold=0.08ns
Hold time slack for back to back flop
scenario with our library
Slack = Clk2q – Hold = +0.03ns
We are “golden” we don’t even have to
worry about this…right?
clk_root
1
2
Any large design will require a clock tree to distribute the clock.
Clock is a large capacitive load. Can’t just drive with one honking driver (RC of wires will kill you then)
Now you have clock skew
set_clock_uncertainty 0.15 clk
Inform Synopsys about your skew

## Slide 23: Hold Time…how do we fix?
clk
clk
Tclk2q=0.11ns
Thold=0.08ns
clk_root
1
2
Slack = Clk2q – Hold – Uncertainty = -0.12ns
-.05
+.10
CTS did the best it could already
Have to add a buffer to slow the
signal down
Referred to as a: min-delay buffer

## Slide 24: Lets Play…fire up design_vision
Code a 64 bit accumulator
read_file –format verilog accum.v
constrain the clock to 2ns and compile
report_area  why are there only 2 combinational cells??
check_design  why are there all these dangling nets?
write –format verilog accum –output accum.vg
ungroup –all –flatten  compile again
report_area again
report_timing –delay max
now constrain clock to 1.5ns and compile again…what did area do
report_timing –delay min
set_clock_uncertainty 0.2 clk
report_timing –delay min  compile agian
report_timing –delay min  Why are there still violators
set_fix_hold clk
compile again

## Slide 25: “Holy Mackerel Batmat, This thing is a monster”
Synopsys is 1 of only 2 significant players in the EDA world
  Any startup with an interesting EDA tool gets “assimulated”
  Their EDA tool offering is vast (many good tools)
    We are only interested in Design Vision/Design Compiler
  Design Compiler is their oldest most used tool (around in one form or another since 1986)
    28 years of development makes for a monster of a CAD tool

## Slide 26: Help!
If you kick off design_vision in GUI mode it has a helpMan Pages in the banner menu
Under this you will find the full list of commands
Yaaa … real fine Hoffman, this only does me good if I know what command I am looking for.

## Slide 27: Help!
Couldn’t remember command name, but knew it
had something to do with uncertainty. Can use wildcard matching with help to get a list of applicable commands.
Once you know the command you can get specific help
design_vision>set_clock_uncertainty -help

## Slide 28: Optimization Priorities
Design rules have priority over timing goals
Timing goals have priority over area goals
  Max delay has priority over min-delay
To prioritize area constraints:
  use the ignore_tns (total negative slack) option when you specify the area constraint:
  set_max_area -ignore_tns 10000
To change priorities use set_cost_priority
  Example: set_cost_priority -delay
Specifies that area is to be prioritized above TNS
prioritizing delay over max transition rules

## Slide 29: Constraints Default Cost Vector

## Slide 30: Compiling the Design
Useful compile options include:
-map_effort low | medium | high (default is medium)
-area_effort low | medium | high (default same as map_effort)
-incremental_mapping (may improve already-mapped)
-verify (compares initial and synthesized designs)
-ungroup_all (collapses all levels of design hierarchy)
New compile_ultra command
  Two pass high effort compile of the design
  May want to compile normally first to get ballpark figure (higher effort == longer compilation)

## Slide 31: Top-Down Compilation
Use top-down compile strategy for medium to small designs
Basic steps are:
  Read in the entire design
  Resolve multiple instances of any design references with uniquify
  Apply attributes and constraints to the top level
  Compile the design using compile or compile_ultra

## Slide 32: Example Top-Down Script
# read in the entire design
read_file -library WORK -format verilog {E.v D.v C.v B.v A.v TOP.v}
current_design TOP
# link TOP.v to libraries and modules it references
Link
# set design constraints
…
set_max_area 2000
# resolve multiple references
uniquify
# compile the design
compile –area_effort high
What??
Will cover this a bit later

## Slide 33: Bottom-Up Compile Strategy
The bottom-up compile strategy
  Compile the subdesigns separately and then incorporate them
  Top-level constraints are applied and the design is checked for violations.
Advantages:
  Compiles large designs more quickly (divide-and-conquer)
  Requires less memory than top-down compile
Disadvantages
  Need to develop local constraints as well as global constraints
  May need to repeat process several times to meet design goals
Only likely to use if running into serious memory or performance issues
This is a royal pain in the butt

## Slide 34: Resolving Multiple References
In a hierarchical design, subdesigns are often referenced by more than one cell instance

## Slide 35: Uniquify Method
The uniquify command creates a uniquely named copy of the design for each instance.
current_design top
uniquify
compile
Each design optimized separately
What are advantages and disadvantages?

## Slide 36: Compile-once-don’t-touch Method
The compile-once-don’t-touch method uses the set_dont_touch command to preserve the compiled subdesign
  current_design top
  characterize –constraints U2/U3
  current_design C
  compile
  current_design top
  set_dont_touch {U2/U3 U2/U4}
  compile
What are advantages and disadvantages?

## Slide 37: Ungroup Method
The ungroup command makes unique copies of the design and removes levels of the hierarchy
  current_design B
  ungroup {U3 U4}
  current_design top
  compile
What are advantages and disadvantages?

## Slide 38: Flattening Hierarchy
module logic1(input a, c, e, output reg x);
always @(a, c, e)
x = ((~a|~c) & e) | (a&c);
endmodule
module logic2(input a, b, c, d, output reg y);
always @(a, b, c, d)
y = ((((~a|~c)&b) | ((a|~b)&c))&d) | ((a|~b)&~d);
endmodule
module logic(input a, b, c, d, e, f, output reg z);
wire x, y;
logic1(a, c, e, x);
logic2(a, b, c, d, y);
always @(x, y, f)
z = (~f&x) | (f&y);
endmodule
Flattened Hierarchy
Area: 34.15
Delay: 0.25
Unflattened Hierarchy
Area: 36.15
Delay: 0.25

## Slide 39: Checking your Design
Use the check_design command to verify design consistency.
  Usually run both before and after compiling a design
  Gives a list of warning and error messages
  Errors will cause compiles to fail
  Warnings indicate a problem with the current design
    Try to fix all of these, since later they can lead to problems
    Use check_design –summary or check_design -no_warnings to limit the number of warnings given
  Use check_timing to locate potential timing problems
  Use report_contraints –all_violators (check everything)

## Slide 40: Analyzing your Design [1]
There are several commands to analyze your design
  report_design
    display characteristics of the current design
    operating conditions, wire load model, output delays, etc.
    parameters used by the design
  report_area
    displays area information for the current design
    number of nets, ports, cells, references
    area of combinational logic, non-combinational, interconnect, total

## Slide 41: Analyzing your Design [2]
  report_hierarchy
    displays the reference hierarchy of the current design
    tells modules/cells used and the libraries they come from
  report_timing
    reports timing information about the design
    default shows one worst case delay path
  report_resources
    Lists the resources and datapath blocks used by the current design
  Can send reports to files
    report_resources > cmult_resources.rpt
Lots of other report commands available

## Slide 42: Optimization Strategies
Area vs. Delay - Often only really optimize for one
  “Fastest given an area constraint”
  “Smallest given a speed constraint”
Design Compiler Reference Manual has several pointers on synthesis settings for these goals