## Slide 1: ECE 551 Digital Design And Synthesis
Spring ‘19
For Loops & Synthesis
Generate Statements
Use of X in Synthesis
Synthesis Pitfalls
Coding for Synthesis

## Slide 2: Administrative Matters
HW4 Moved to Friday Apr 5th@ class
Have you formed your project team and come up with a team name?
Video Lectures for Lecture8 are posted. There will be a quiz on Monday

## Slide 3: For Loops & Synthesis
Can a For Loop be synthesized?
reg [15:0] countmem [0:7];
integer x;
always @(posedge clk) begin
for (x = 0; x < 8; x = x + 1) begin
countmem[x] <= countmem[x] +1;
end
end
  Yes, if it is fixed length
  The loop is “unrolled”
How do you think this code would synthesize?

## Slide 4: For Loops & Synthesis
What if loop upper limit was a parameter?
These loops are unrolled when synthesized
  That’s why they must be fixed in length!
  Loop index is type integer but it is not actually synthesized
  Example creates eight 16-bit incrementers.
+1
16
countmem[0]
16
clk
+1
16
countmem[1]
16
clk
…
+1
16
countmem[7]
16
clk

## Slide 5: Unnecessary Calculations
Expressions that are fixed in a for loop are replicated due to “loop unrolling.”
Solution: Move fixed (unchanging) expressions outside of all loops.
for (x = 0; x < 8; x = x + 1) begin
for (y = 0; y < 8; y = y + 1) begin
index = x*8 + y;
value = (a + b)*c;
mem[index] = value;
end
end
This is just basic common sense, and applies to any language (in a programming language you would be wasting time, not hardware).
Yet this is a common mistake
Which expression(s) should be moved?

## Slide 6: More on Loops & Synthesis
A loop is static (data-independent) if the number of iterations is fixed at compile-time
Loop Types
  Static without internal timing control
    Combinational logic
  Static with internal timing control (i.e. @(posedge clk))
    Sequential logic
  Non-static without internal timing control
    Not synthesizable
  Non-static with internal timing control (i.e. @(posedge clk))
    Sometimes synthesizable, Sequential logic

## Slide 7: Static Loops w/o Internal Timing
Combinational logic results from “loop unrolling”
Example
  always@(a) begin
  andval[0] = 1;
  for (i = 0; i < 4; i = i + 1)
  andval[i + 1] = andval[i] & a[i];
  end
What would this look like?
For registered outputs:
  Change sensitivity list ‘a’ with ‘posedge clk’

## Slide 8: Static Loops with Internal Timing
If a static loop contains an internal edge-sensitive event control expression, then activity distributed over multiple cycles of the clock
  always begin
  for (i = 0; i < 4; i = i + 1)
  @(posedge clk) sum <= sum + i;
  end
What does this loop do?
Does it synthesize?...Yes, but…

## Slide 9
Number of iterations is variable
  Not known at compile time
Can be simulated, but not synthesized!
Essentially an iterative combinational circuit of data dependent size!
always@(a, n) begin
andval[0] = 1;
  for (i = 0; i < n; i = i +1)
  andval[i + 1] = andval[i] & a[i];
  end
What if n is a parameter?
Non-Static Loops w/o Internal Timing

## Slide 10: Non-Static Loops with Internal Timing
Number of iterations determined by
  Variable modified within the loop
  Variable that can’t be determined at compile time
Due to internal timing control—
  Distributed over multiple cycles
  Number of cycles determined by variable above
Variable must still be bounded
always begin
continue = 1’b1;
  while (continue) begin
  @(posedge clk) sum = sum + in;
  if (sum > 8’d42) continue = 1’b0;
  end
end
Can this be synthesized?
What does it synthesize to?
Who really cares!
This is a stupid way to do it!
Use a SM.

## Slide 11: Any loop with internal timing can be done as a SM
module sum_till (clk,rst_n,sum,in);
input clk,rst_n;
input [5:0] in;
output [5:0] sum;
always @(posedge clk or negedge rst_n)
if (~rst_n)
sum <= 6’h00;
else if (en_sum)
sum <= sum + in
assign en_sum = (sum<6’d43) ? 1’b1 : 1’b0;
endmodule
Previous example didn’t really even require a SM.
This code leaves no question how it would synthesize.
RULE OF THUMB:
If it takes you more than 15 seconds to conceptualize how a piece of code will synthesize, then it will probably confuse Synopsys too.

## Slide 12: FSM Replacement for Loops
Not all loop structures supported by vendors
Can always implement a loop with internal timing using an FSM
  Can make a “while” loop easily
  Often use counters along with the FSM
All synthesizers support FSMs!
Synopsys supports for-loops with a static number of iterations
State3
condition
condition

## Slide 13: Generated Instantiation
Generate statements  control over the instantiation/creation of:
    Modules
    UDPs & gate primitives
    continuous assignments
    initial blocks & always blocks
Generate instantiations resolved during “elaboration” (compile time)
    When module instantiations are linked to module definitions
    Before the design is simulated or synthesized – this is NOT dynamically created hardware

## Slide 14: Generate-Loop
A generate-loop permits making one or more instantiations (pre-synthesis) using a for-loop.
module gray2bin1 (bin, gray);
parameter SIZE = 8; // this module is parameterizable
output [SIZE-1:0] bin; input [SIZE-1:0] gray;
genvar i;
generate
for (i=0; i<SIZE; i=i+1) begin: bit
assign bin[i] = ^gray[SIZE-1:i]; \\ Data Flow replication
end
endgenerate
endmodule
Does not exist during simulation of design
Typically name the generate as reference

## Slide 15: Generate Loop
Is really just a code replication method. So it can be used with any style of coding. Gets expanded prior to simulation.
module replication_struct(i0, i1, out);
parameter N=32;
input [N-1:0] i1,i0;
output [N-1:0] out;
genvar j;
generate
for (j=0; j<N; j=j+1)
begin : xor_loop
xor g1 (out[j],in0[j],in1[j]);
end
endgenerate
endmodule
Structural replication
Hierarchical reference to these instantiated gates will be:
…xor_loop[0].g1
…xor_loop[1].g1
.
.
.
…xor_loop[31].g1

## Slide 16: Generate-Conditional
A generate-conditional allows conditional (pre-synthesis) instantiation using if-else-if constructs
module multiplier(a ,b ,product);
parameter a_width = 8, b_width = 8;
localparam product_width = a_width+b_width;
input [a_width-1:0] a; input [b_width-1:0] b;
output [product_width-1:0] product;
generate
if ((a_width < 8) || (b_width < 8))
CLA_multiplier #(a_width,b_width) u1(a, b, product);
else
WALLACE_multiplier #(a_width,b_width) u1(a, b, product);
endgenerate
endmodule
These are parameters, not variables!

## Slide 17: Generate-Case
A generate-case allows conditional (pre-synthesis) instantiation using case constructs
See Standard 12.1.3 for more details
module adder (output co, sum, input a, b, ci);
parameter WIDTH = 8;
generate
case (WIDTH)
1: adder_1bit x1(co, sum, a, b, ci); // 1-bit adder implementation
2: adder_2bit x1(co, sum, a, b, ci); // 2-bit adder implementation
default: adder_cla #(WIDTH) x1(co, sum, a, b, ci);
endcase
endgenerate
endmodule
Of course case selector has to be deterministic at elaborate time, can not be a variable. Usually a parameter.

## Slide 18: Synthesis of x and z
Only allowable uses of x is as “don’t care”, since x cannot actually exist in hardware
  in casex
  in defaults of conditionals such as :
    The else clause of an if statement
    The default selection of a case statement
Only allowable use of z:
  Constructs implying a 3-state output
    Of course it is helpful if your library supports this!

## Slide 19: Don’t Cares
x, ?, or z within case item expression in casex
  Does not actually output “don’t cares”!
  Values for which input comparison to be ignored
  Simplifies the case selection logic for the synthesis tool
1 | 1 | 1 | 1
0 | 0 | 1 | 1
casex (state)
3’b0??: out = 1’b1;
3’b10?: out = 1’b0;
3’b11?: out = 1’b1;
endcase
state[1:0]
state[2]
00
01
11
10
0
1
out = state[2] + state[1]

## Slide 20: Use of Don’t Care in Outputs
Can really reduce area
case (state)
3’b001: out = 1’b1;
3’b100: out = 1’b0;
3’b110: out = 1’b1;
default: out = 1’b0;
endcase
0 | 1 | 0 | 0
0 | 0 | 0 | 1
state[1:0]
state[2]
00
01
11
10
0
1
case (state)
3’b001: out = 1’b1;
3’b100: out = 1’b0;
3’b110: out = 1’b1;
default: out = 1’bx;
endcase
x | 1 | x | x
0 | x | x | 1
state[1:0]
state[2]
00
01
11
10
0
1

## Slide 21: Unintentional Latches
  assign y = b | z;
z
y
a
b
Avoid structural feedback in continuous assignments, combinational always
  assign z = a | y;
For conditional assignments, either:
  Set default values before statement
  Make sure LHS has value in every branch/condition
For warning, set hdlin_check_no_latch true before compiling

## Slide 22: Synthesis Example [1]
module Hmmm(input a, b, c, d, output reg out);
always @(a, b, c, d) begin
if (a) out = c | d;
else if (b) out = c & d;
end
endmodule
Area = 44.02
How will this synthesize?
a|b enables latch
Either c|d or c&d are passed through an inverting mux depending on state of a / b

## Slide 23: Synthesis Example [2]
module Better(input a, b, c, d, output reg out);
always @(a, b, c, d) begin
if (a) out = c | d;
else if (b) out = c & d;
else out = 1’b0;
end
endmodule
Area = 16.08
Perhaps what you meant was that if not a or b then out should be zero??
Does synthesize better…no latch!

## Slide 24: Synthesis Example [3]
module BetterYet(input a, b, c, d, output reg out);
always @(a, b, c, d) begin
if (a) out = c | d;
else if (b) out = c & d;
else out = 1’bx;
end
endmodule
Area = 12.99
But perhaps what you meant was if neiter a nor b then you really don’t care what out is.
Hey!, Why is b not used?

## Slide 25: Gated Clocks
Use only if necessary (e.g., for low-power)
  Becoming more necessary with demand for many low power products
clk
clk_en
This clock arrives later than the system clock it was derived from. We just created a min-delay problem. (race condition) (shoot through)
Min_delay_slack = clk2q – THold – Skew_Between_clks

## Slide 26: Gated Clocks (not so simple)
Something this simple does not work. Recall the enable function is probably coming from a SM. So it changes slightly after the rising edge of clock.
clk
clk_en
resulting gated clock
That’s pretty messed up!

## Slide 27: Gated Clocks (do it this way)
clk
clk_en
resulting gated clock
Have to use an enable low latch to latch the clock enable signal. This ensures the enable is setup and ready for the next high phase of clock
Have to balance from clock root to all leaf nodes of clock

## Slide 28: Gated Clocks
Gated clock domains can’t be treated lightly:
1.) Skew between domains
2.) Loading of each domain. How much capacitance is on it? What is its rise/fall times
3,) RC in route. Is it routed in APR like any old signal, or does it have priority?
Clocks are not signals…don’t treat them as if they were.
1.) Use clock tree synthesis (CTS) within the APR tool to balance clock network (usually the job of a trained APR expert)
2.) Paranoid control freaks (like me) like to generate the gated domains in custom logic (like clock reset unit). Then let CTS do a balanced distribution in the APR tool.

## Slide 29: Chain Multiplier
module mult(output reg [31:0] out, input [31:0] a, b, c, d);
always@(*) begin
out = ((a * b) * c) * d;
end
endmodule
Area: 47381
Delay: 8.37

## Slide 30: Tree Multiplier
module multtree(output reg [31:0] out, input [31:0] a, b, c, d);
always@(*) begin
out = (a * b) * (c * d);
end
endmodule
Area: 47590
Delay: 5.75 vs 8.37

## Slide 31: Multi-Cycle Shared Multiplier
module multshare(output reg [31:0] out,
input [31:0] in, input clk, rst);
reg [1:0] cycle;
wire [31:0] multval;
always @(posedge clk)
if (rst) cycle <= 0;
else cycle <= cycle + 1;
always @(posedge clk)
out <= multval;
assign multval = (|cycle) ? out*in : in;
endmodule

## Slide 32: Multi-Cycle Shared Multiplier (results)
Area: 15990 vs 47500
Delay: 4*3.14
4 clocks, minimum period 3.14

## Slide 33: Shared Conditional Multiplier
module multcond1(output reg [31:0] out,
input [31:0] a, b, c, d, input sel);
always @(*) begin
if (sel) out = a * b;
else out = c * d;
end
endmodule
Mutually exclusive use of the multiply
Area: 15565
Delay: 3.14

## Slide 34: Selected Conditional Multiplier [1]
module multcond2(output reg [31:0] out,
input [31:0] a, b, c, d, input sel);
wire [31:0] m1, m2;
assign m1 = a * b;
assign m2 = c * d;
always @(*) begin
if (sel) out = m1;
else out = m2;
end
endmodule

## Slide 35: Selected Conditional Multiplier [2]
Area: 30764 vs. 15565
Delay: 3.02 vs. 3.14
Why is the area larger?

## Slide 36: Conditional Multipler – One More Time
If you know ahead of time that you want two muxes and one multiplier, describe that directly!
Don’t rely on the synthesis tool to improve inefficient HDL; describe what you want first.
Caveat: You have to know what you want.
module multcond2(output reg [31:0] out,
input [31:0] a, b, c, d, input sel);
wire [31:0] op1, op2;
assign op1 = sel ? a : c;
assign op2 = sel ? b : d;
always @(*) begin
out = op1 * op2;
endmodule

## Slide 37: Decoder Using Indexing
What does synthesis do?
Think of Karnaugh Map

## Slide 38: Decoder Using Loop
For this implementation how are we directing synthesis to think?
Assign each bit to digital comparator result

## Slide 39
Decoder Verilog: Timing Comparison
Loop method
Starts to look advantageous

## Slide 40: Decoder Verilog: Area Comparison
Loop method
Starts to look advantageous

## Slide 41: Decoder Verilog: Compile Time Comparison
Holy Mackerel Batman!
What is synthesis doing?
Why is it working so long and hard?
Looking for shared terms

## Slide 42: Late-Arriving Signals
After synthesis, we will identify the critical path(s) that are limiting the overall circuit speed.
It is often that one signal to a datapath block is late arriving.
This signal causes the critical path…how to mitigate?:
  Circuit reorganization
    Rewrite the code to restructure the circuit in a way that minimizes the delay with respect to the late arriving signal
  Logic duplication
    This is the classic speed-area trade-off. By duplicating logic, we can move signal dependencies ahead in the logic chain.

## Slide 43: Logic Reorganization Example [1]

## Slide 44: Logic Reorganization Example [2]
What can we do if A is the late-arriving signal?

## Slide 45: Logic Reorganization Example [3]
That’s right! We have to do the math, and re-arrange the equation so the comparison does not involve and arithmetic operation on the late arriving signal.

## Slide 46: Logic Reorganization Example [4]
Why the area improvement?
Synopsys didn’t spend so much effort upsizing gates to try to make transisitons faster. This new design is faster, lower area, and lower power

## Slide 47: Logic Duplication Example [1]

## Slide 48: Logic Duplication Example [2]
What if control is the late arriving signal?

## Slide 49: Logic Duplication Example [3]

## Slide 50: Logic Duplication Example [4]

## Slide 51: Exercise
Assume we are implementing the below code, and cin is the late arriving signal? How can we optimize the resulting hardware for speed? At what cost?
reg [3:0] a, b;
reg [4:0] y;
reg cin;
y = a + b + cin;

## Slide 52: Exercise
Revise to maximize performance wrt late
reg [3:0] state;
reg late, y, x1, x2, x3;
case(state)
SOME_STATE:
if (late) y = x1;
else y = x2;
default:
if (late) y = x1;
else y = x3;
endcase
Actually, there is nothing you can really do here. This is simple boolean logic, and synopsys already does a good job optimizing for late arriving.
Coding optimizations often apply more to larger functions (like arithmetic operations, & comparisons). Than to boolean logic.

## Slide 53: Mixing Flip-Flop Styles (1)
What will this synthesize to?
module badFFstyle (output reg q2, input d, clk, rst_n);
reg q1;
always @(posedge clk)
if (!rst_n)
q1 <= 1'b0;
else begin
q1 <= d;
q2 <= q1;
end
endmodule
If !rst_n then q2 is not assigned…
It has to keep its prior value

## Slide 54: Flip-Flop Synthesis (1)
Area = 59.0
Note: q2 uses an enable flop (has mux built inside)
enabled off rst_n

## Slide 55: Mixing Flip-Flop Styles (2)
module goodFFstyle (output reg q2, input d, clk, rst_n);
reg q1;
always @(posedge clk)
if (!rst_n) q1 <= 1'b0;
else q1 <= d;
always @(posedge clk)
q2 <= q1;
endmodule
Only combine like flops (same reset structure) in a single always block.
If their reset structure differs, split into separate always blocks as shown here.

## Slide 56: Flip-Flop Synthesis (2)
Area = 50.2 (85% of original area)
Note: q2 is now just a simple flop as intended

## Slide 57: Flip-Flop Synthesis (3)
Using asynchronous reset instead
  Bad (same always block): Area = 58.0
  Good (separate always block): Area = 49.1
Note asynch area less than synch, and cell count less (less interconnect)

## Slide 58: Conclusions
The designer is responsible for some optimizations that cannot be achieved by the synthesis tool.
It takes a lot of knowledge to be an expert designer
  Hardware Design
  HDL
  Synthesis Tool
One of the largest roles of the designer is to understand tradeoffs and make appropriate decisions