## Slide 1: ECE 551 Digital Design And Synthesis
Spring ‘19
Synthesis Flow
Synthesis Optimizations

## Slide 2: Administrative Matters
HW5 Due Fri Apr 19th
Have you read the project spec yet? … it is posted at bottom of Canvas page

## Slide 3
Internal Synthesizer Flow
Parsing and
Syntax & Semantic
Error Checking
Translation
(Elaboration)
Synthesizer
Policy Checking
Architectural
Optimization
Multi-Level Logic
Optimization
Technology
Mapping
Technology-Based
Implementation
(netlist)
Technology
Library
Structural
Representation
HDL Description

## Slide 4: Initial Steps (Analyze Verilog File)
Parsing for Syntax and Semantics Checking
  Gives error messages and warnings to user
  User may modify the HDL description in response
Synthesizer Policy Checking
  Check for adherence to allowable language constructs
  Check for usage recommendations
This is where you find out you can’t use certain Verilog constructs
This is synthesizer-dependent
  Example: Design Vision allows indexed part-select (guess[i*2 : 2]), but the Xilinx tool does not
  Certain things common to MOST synthesizers

## Slide 5: Translation (Elaboration)
Unrolls loops, substitutes macros & parameters, computes constant functions, evaluates generate conditionals
Builds a structural representation of the design
Like a netlist, but includes larger components
  Not just gate-level, may include adders, etc.
Gives additional errors or warnings to the user
  Issues in initial transformation to hardware.
Affects quality achieved by optimization steps
  Structural representation depends on HDL quality
  Poor HDL can prevent optimization

## Slide 6: Importance of Translation
It is important for the tool to recognize the sort of logic structures you are trying to describe.
If it sees a 32-bit full adder, the tool has built-in solutions for optimizing adders
  Ripple-carry, carry-save, carry look-ahead, etc.
If it just sees a Boolean function with 65 inputs, it has to work a lot harder to achieve the same results
  Do you think it can invent a CLA on the fly?

## Slide 7: Optimization in Synthesis
None of these are guaranteed!
  Most synthesizers will make at least some attempt
Detect and eliminate redundant logic
Detect combinational feedback loops
Exploit don't-care conditions
Try to detect unused states (logic states you can’t get to)
Synthesize optimal, multilevel realizations subject to:
  constraints on area and/or speed
  available technology (library)

## Slide 8: Optimization Process
Optimization modifies the initial netlist resulting from elaboration.
  Architecture choices made first (CLA,RCA,…)
  Boolean logic level optimization next
  Maps to cells from the technology library
  Attempts to meet all specified constraints
The process is divided into major phases
  All or some selection of the major phases may be performed during optimization
  Phase selection can be controlled by the user

## Slide 9: Optimization Phases
Architectural optimization
  High-level optimizations that occur before the design is mapped to the logic-level
  Based on constraints and high-level coding style
  Level of parallelism?
  Building block choices like adder architecture (DW components)
  After optimization circuit function is represented by a generic, technology-independent netlist (GTECH)

## Slide 10
In Synopsys, types include:
  Sharing common mathematical subexpressions
  Sharing resources
  Selecting DesignWare implementations
  Reordering operators
  Identifying arithmetic expressions for datapath synthesis
Architectural Optimization

## Slide 11: Architectural Optimization
Examples:
  Replace an adder used as a counter with incrementor
  Replace adder and separate subtractor with adder/subtractor if not used simultaneously
    if (~sub) z = a + b; else z = a – b;
  Performs selection of pre-designed components (Synopsys DesignWare)
    adders, multipliers, shifters, comparators, muxes, etc.
Need good code for synthesizer to do this
Designer still knows more about the project

## Slide 12: Logic/Gate-Level Optimization
Works on the generic netlist created by logic synthesis
Produces a technology-specific netlist.
In Synopsys, it consists of four stages:
  Mapping
  Delay optimization
  Design rule fixing
  Area optimization
This phase often runs in multiple iterations if constraints are not met on the first try

## Slide 13: Logic/Gate-Level Optimization
Mapping
  Generates a gate level implementation
  Tries to meet timing and area goals
Delay optimization
  Tries to fix delay violations from mapping phase.
  Does not fix design rule violations or meet area constraints.
Design rule fixing
  Tries to correct design rule violations
    Inserting buffers or resizing existing cells
  If necessary, violates optimization constraints
Area optimization
  Tries to meet area constraints, which have lowest priority

## Slide 14: Combinational Optimization
Boolean equation manipulation
  Boolean reduction
  Factoring
  Sharing common terms
Mapping Optimizations
  Gate mapping based on CF
  Applying De-Morgans
  Sizing Gates & Buffering

## Slide 15: Gate-Level Optimization

## Slide 16: Logic-Level Optimizations
Verilog
Description
Technology
Implementation
TRANSLATION
ENGINE
Two-level
Logic Functions
Optimized
Multi-level Logic
Functions
OPTIMIZATION
ENGINE
MAPPING
ENGINE
Technology
Libraries

## Slide 17: Logic Optimizations
Area
  Number of gates fewer == smaller
  Fan in of gates (# inputs) fewer == smaller
  Drive Strength (transistor width) narrower == smaller
Delay
  Number of logic levels fewer == faster (usually)
  Fan in of gates (# inputs) fewer == faster
Gate Effort  Summation of Fan in of gates needed to implement function
Note that examples that follow ignore NOT gates for gate count / levels of circuits

## Slide 18: Logic Optimizations
Decomposition
Extraction
Factoring
Substitution
Elimination
You don’t have to remember the names of these
But understand the concept and the motivation

## Slide 19: Decomposition
Find common expressions
Reduce redundancy
  Reduce area (number/size of gates)
May increase delay
  More levels of logic

## Slide 20: Decomposition Example
F = abc + abd + a’c’d’ + b’c’d’ ~7 gates, ~3 levels
F = ab(c + d) + c’d’(a’ + b’)
F = ab(c + d) + (c + d)’(ab)’
X = ab 1 gate, 1 level
Y = c + d 1 gate, 1 level
F = XY + X’Y’ 3 gates, 3 levels (or what?)
Gate Effort = 4*(3-input AND) + 4-input OR = 16 effort
Gate Effort = 2-input AND + 2-input OR + 2*(2-input AND) + 2-input OR = 10 effort

## Slide 21: Extraction
Find common sub-expressions in functions
Like decomposition, but across more than one function
Reduce redundancy
  Reduce area (number/size of gates)
May increase delay if more logic levels introduced

## Slide 22: Extraction Example
F = (a + b)cd + e 3 gates, 3 levels
G = (a + b) e’ 2 gates, 2 levels
H = cde 1 gate, 1 level
Define common terms: X = a + b, Y = cd 1 gate, 1 level (each)
F = XY + e 3 gates, 3 levels
G = Xe’ 2 gate, 2 levels
H = Ye 2 gate, 2 levels
Before:
  (3) 2-input ORs, (2) 3-input ANDs, (1) 2-input AND
  Gate Effort = 6 + 6 + 2 = 14
After
  (2) 2-input ORs, (4) 2-input ANDs
  Gate Effort = 4 + 8 = 12

## Slide 23: Factoring
Traditional two-level logic is sum-of-products
Sometimes better expressed by product-of-sums
  Fewer literals => less area
May increase delay if logic equation not completely factored (becomes multi-level)

## Slide 24: Factoring Example
Definitely good:
  F = ac + ad + bc + bd Gate Effort = 8 + 4
  F = (a + b)(c + d) Gate Effort = 4 + 2
Maybe good:
  F = ac + ad + e Gate Effort = 7
  F = a(c + d) + e Gate Effort = 6
  Factoring may improve area...
  But will likely increase delay (tradeoff)

## Slide 25: Substitution
Similar to Extraction (in fact a sub-case of extraction)
When one function is subfunction of another
Reduce area
  Fewer gates
Can increase delay if more logic levels

## Slide 26: Substitution Example
G = a + b 1 gate, 1 level
F = a + b + c 1 gate, 1 level
F = G + c 2 gate, 2 levels
Before:
  (1) 2-input OR, (1) 3-input OR => Gate Effort = 5
After
  (2) 2-input ORs (but increased levels) => Gate Effort = 4

## Slide 27: Elimination (Flattening)
Opposite of previous optimizations
Goal is to reduce delay
  Make signals travel though as few logic levels as possible
But will likely increase area
  Gate replication / redundant logic

## Slide 28: Elimination Example
G = c + d 1 gate, 1 level
F = Ga + G' b 3 gates, 3 levels
G = c + d 1 gate, 1 level
F = ac + ad + bc’d’ 4 gates, 2 levels
Before:
  (2) 2-input ORs, (2) 2-input ANDs
After:
  (1) 2-input OR, (1) 3-input OR, (2) 2-input ANDs, (1) 3-input AND (but fewer levels)

## Slide 29: compile_ultra Optimizations
High effort, maximum optimization
Automatic hierarchical ungrouping
  Ungroups small modules before mapping
  Ungroups critical path based on delay
Automatic datapath extraction
  E.g. carry-save adders
Boundary optimization
  Propagates logic across hierarchical boundaries (constants, NC inputs/outputs, NOT)
Sequential inversion
  Sequential elements can have their outputs inverted

## Slide 30: How to Ensure a Job Offer Once You Have the on-site Interview

## Slide 31: Sharing and Unsharing
Expression sharing may be overridden later due to timing
  Z1 <= A + B + C
  Z2 <= A + B + D
  Arrival time is A < B < D < C
A
C

## Slide 32: Sharing and Unsharing
Mutually exclusive operations can share resources
  if(SEL) Z = A + B
  else Z = C + D

## Slide 33: Sequential Inversion
set compile_seqmap_enable_output_inversion true
Allows the mapping of sequential elements in the design to library cells whose outputs are inverted.
This can reduce area and or speed
Not applicable for compile_ultra, because compile_ultra already does this.

## Slide 34: Register Retiming
At the HDL level, determining the optimal placement of registers is difficult and tedious at best, or just plain impossible at worst
The register retiming tool moves registers through the synthesized combinational logic network to improve timing and/or area
  Equalize delay (i.e. reduce critical path delay by increasing delay in other paths)
  Reduce the number of flip-flops if timing criteria are met
    Usually propagate registers forward
Can also automatically pipeline combinational logic modules

## Slide 35: Register Retiming Example [1]
optimize_registers is the command in Design Compiler

## Slide 36: Register Retiming Example [2]
Personally: I would never use this. I have an inherent mis-trust of CAD tools. I would never let it move any of my flops, and certainly never trust it to rearrange my pipelined processor.