## Slide 1: ECE 551 Digital Design And Synthesis
Spring ‘19
Parasitic Capacitance
SDF & Back Annotation

## Slide 2: Administrative Matters
HW5 is assigned and due Fri April 19th.
  Most of it is as team, but prob 1 is individual

## Slide 3
Any two conducting geometries separated by an insulator will have capacitance between them.
Capacitance is Unavoidable
In digital circuits capacitances slow the circuit down.
Time to charge a capacitance C to a voltage V is proportional to C.
More cap  Slower charge up
Unavoidable & Undesireable:
Any questions on why we call it parasitic capacitance?

## Slide 4: What do Our Parasitics Look Like?
Wisconsin’s
most prevalent
No…I meant on
an integrated circuit

## Slide 5: Modern Processes Are Worse
As technologies scaled smaller the aspect ratio of the wires changed. Typical wire is now “taller” than it is wide.
As the spacing shrank the height did not shrink, or even grew to try to recoup some of the conductance lost by narrowing the line.
P- Substrate
SiO2
Fringe components and
line to line components
now dominate. Parallel
plate is a small percent of
the total cap.

## Slide 6: Cap to ground & Cap to neighbors
0.2
0.4
0.6
0.8
1
2
3
CTOTAL
CGROUND
CLINE-LINE
Design Rule (m)
Capacitance (pF/cm)
This graph is for the
middle conductor
“sandwiched” between
two other conductors
at minimum spacing.
Not only is this sidewall and fringing capacitance brining the total cap higher, but it creates a whole new noise problem called cross-talk due to the line to line capacitances.

## Slide 7: How do we Simulate this Effect?
Synopsys Doesn’t Have a Clue
  Sad reality is wireload model is a S.W.A.G.
  Might as well go ask the local fortune teller if your circuit is going to work
Need to extract the value of parasitic capacitance from actual layout of the circuit.
  Since parasitics are dominated by wiring, the wiring has to be routed to extract it.
  Need to perform APR first!

## Slide 8
What is an APR (Auto Place & Route) Block?
  Netlist mapped to standard logic cells (from synthesis tool) is read into a CAD tool.
  Standard Cells (typically of a fixed height) are placed by an automated program in
  cell rows (Place)
  Then they are interconnected (Route)

## Slide 9
Does it remove the parasitics?
  Quit asking stupid questions…”I cannot change the laws of physics Captain”
No, it just reads all the geometries of the interconnecting and overlapping metal layers that wire up the standard cells in the APR blocks
It analyzes these geometries and extracts the value of the parasitic capacitances
What is a Parasitic Extractor

## Slide 10: What is Done with These Values?
Extracted Parasitic values used here
A file called a .SDF file is generated
SDF = Standard Delay Format
The functionality of this “Timing Calculator” is typically built into the APR tool
The analysis tool can be ModelSim
ModelSim can read .SDF files.

## Slide 11: Post Layout Simulation
This whole process of analyzing with extracted parasitics is often referred to as “back annotation”
Back annotation of parasitics can be to dynamic or static timing analysis tools
  Static timing analysis tools are like what Synopsys does
    Timing reports like Synopsys shows for max and min paths
    NanoTime (also a Synopsys tool) is a really good static timing analysis tool
  ModelSim can accept .SDF files for back annotation of parasitics.
    Now you would re-run some/all of your tests with this timing back annotated. (This is dynamic simulation)

## Slide 12: What Does This SDF File Look Like?
PVT for which the delay data was
calculated, is specified in header
Cell instance for which this data applies
clk2q delay (min:typ:max)
(use min for hold-time checking)
(use max for setup-time checking)
clr2q delay (asynch reset to Q out)

## Slide 13: Parasitics Don’t Just Slow Down Cells
Resistance:
  When Rdriver >> Rwire then it is not useful to look at interconnect in terms of
  RC. Lumped capacitance works fine.
  Now that chips are larger and drivers are faster these RC components become
  significant.
Consider a 2000m M2 line at 0.18u wide. The route it self has a 0.45pF capacitance. It
drives a 0.3pF load. The resistance M2 = 19mW/sq.
0.45pF
211W
0.3pF
0.69RC = 0.11ns
If your targeting
1GHz this is over
10% of your period
Wires have delay too…RC Delay

## Slide 14: SDF Can Handle Wire RC Delay Too
The timing calculation tool can calculate RC delays of intecconnects between cells.
It uses both the extracted parasitic capacitance data, as well as extracted resistance data.
SDF file has an INTERCONNECT delay specifier

## Slide 15: How Do I Use SDF with Verilog?
Back annotate SDF to your post-synthesis (gate level) netlist simulation.
  Now you will be simulating with accurate timing
  Simulate your test suite (or a least a large fraction of it)
    Simulate at typical delays to sanity check the whole environment
    Simulate at max delays to stress setup times
    Simulate at min delays to stress hold times
Verilog contains a directive: $sdf_annotate to control .SDF back annotation.
$sdf_annotate ("sdf_file" [ , [ module_instance ] [ , [ "config_file" ]
[ , [ "log_file" ] [ , [ "mtm_spec" ]
[ , [ "scale_factors" ] [ , [ "scale_type" ] ] ] ] ] ] ] );

## Slide 16: How Do I Use SDF with Verilog?
module testbench();
// $sdf_annotate(“~ehoffman\verilog\dig_core_sss.sdf”,testbench.idig_core);
$sdf_annotate(“~ehoffman\verilog\dig_core_fff.sdf”,testbench.idig_core);
// $sdf_annotate(“~ehoffman\verilog\dig_core_typ.sdf”,testbench.idig_core);
dig_core idig_core(.clk(clk), .por_n(por_n), .dst(dst), …
.
.
.
endmodule
Example: Your APR tool created 3 separate files for max/typ/min delays of your digital core (dig_core). (sss=slow,slow,slow PVT), (fff=fast,fast,fast PVT)
Inside the testbench code you apply the SDF to the instance of the digital core. You have 3 such $sdf_annotate lines and just comment out the ones you are not simulating.

## Slide 17: Refining your S.W.A.G.
Extracted
Parasitics
Physical Synthesis
EDA Tool
(APR tool or
Synopsys option)
Post APR
Netlist
Refined
Wireload
model
Synopsys
or other synthesis
tool
Verilog
Code
Constraints
New
Gatelevel
Netlist
Back to APR