## Slide 1: ECE 551 Digital Design And Synthesis
Spring ‘19
Digital Circuit Implementations:
  Standard Cell
  FPGA
  Custom Logic

## Slide 2: Administrative Matters
Project Demos (all team members should be present)
  Weds May 1st 1:00PM till evening B555 (1.5% extra)
  Thurs May 2nd 1:00PM till evening B555 (0.75% extra)
  Fri May 3rd 1:00PM till evening B555
Final Monday May 6th, 2:45PM Room ???
  Comprehensive with focus on Lecture 6 – 12
  Can have a 8.5x11 cheatsheet
  Prior exam will be posted (and reviewed during last discussion section)

## Slide 3
After synthesis, implement as hardware
  FPGAs
  Standard cells
  Custom logic
Choose implementation based on cost and performance requirements
Functional & Synthesized…Now What?

## Slide 4: FPGAs
Field Programmable Gate Array
  Temporary (SRAM based)
  Permanent (Flash) not as common
Pros
  Allow for very complex implementations
  Generally reuseable (upgrades/bugfixes/prototype)
  Low non-recurring engineering costs (NREs)
Cons
  Expensive per-unit (10s-100s of $)
  Slower than gates
  Need support circuits (configuration loading)
  Higher power consumption than ASIC.
  Not as robust (mission critical operations)

## Slide 5: Programming an FPGA
Most designs based on SRAM
  Writing to the SRAM “configures” device
  Different circuits implemented based on values
DATA
READ or WRITE
Q
Q

## Slide 6: Configurable Routing Elements
Programmable connection
Programmable bypass
Routing
Resource #1
P
Routing
Resource #2
DFF
OUT
SIGNAL
P

## Slide 7: Logic Elements
Look-Up Table (LUT)
  Essentially a very small memory
  Most common size is 4-input LUT (shown is 3-input)
P1
P2
P3
P4
P5
P6
P7
P8
a
c
b
OUT
0
1
2
3
4
5
6
7

## Slide 8
Look-Up Table (LUT)
  OUT = a XOR b XOR c
abc | OUT
000 | 0
001 | 1
010 | 0
011 | 1
100 | 0
101 | 1
110 | 0
111 | 1
Logic Elements
0
1
0
1
0
1
0
1
a
c
b
OUT
0
1
2
3
4
5
6
7

## Slide 9: Logic Elements
Look-Up Table (LUT)
  OUT = ab + ac + bc
abc | OUT
000 | 1
001 | 0
010 | 1
011 | 1
100 | 1
101 | 1
110 | 0
111 | 1
1
0
1
1
1
1
0
1
a
c
b
OUT
0
1
2
3
4
5
6
7

## Slide 10: Logic Elements
Look-Up Table (LUT)
  Extremely flexible in implementing logic
  Larger and slower than just using gates
P1
P2
P3
P4
P5
P6
P7
P8
a
c
b
OUT
0
1
2
3
4
5
6
7

## Slide 11: FPGA Logic Structure
“Cell” or “logic block”:
  1 or more LUTs (generally 4-input)
  At least one D flip-flop
  Possibly fast carry logic
Connect several logic blocks to form circuit
4-LUT
carry logic
Cout
Cin
OUT
DFF
I1 I2 I3 I4

## Slide 12: Xilinx 4000 Combinational Logic Block

## Slide 13: Xilinx 4000 FPGA
Really much more than 4 CLB’s and 9 configurable routing channels but this gives an idea of the structure

## Slide 14: FPGAs
Allow for complex implementations
Generally reuseable (upgrades/bugfixes/prototype)
Low non-recurring engineering costs (NREs)
Expensive per-unit (10s-100s of $)
Slower than gates (Programming points)
Newer FPGAs often incorporate memories, multipliers, peripherals, and even processors all on the same chip

## Slide 15: Standard Cells
Gates and other small structures
Can also use macroblocks
  Groups of pre-optimized cells
  Larger custom-layout structures
  More efficient when possible
From: http://www.zuraleff.com/layout

## Slide 16: Standard Cell Layouts
…
Adjustable Spacing
Megacells
Metal interconnect placed in channels between cells
Gate, flip-flop, 1-bit adder, …

## Slide 17: Standard Cells
Cheap per-unit pricing ($0.50-$10s)
Fast compared to FPGAs
High NREs (design time, mask fabrication...)
  $150K-$10M
  Cost of a respin is very high in time & $$
Only makes sense for
  Large quantities and/or
  Critical operations

## Slide 18: Custom Logic
Manual layout
Very high NREs
  Huge design time!
  Design changes painful.
Human is still better than the CAD tool at tight layout.
There exists a compromise between standard cell APR and full custom. These datapath synthesis tools do APR on a bitslice basis exploiting symmetry in the netlist.

## Slide 19
Apple A6 Utilizes Full Custom Design

## Slide 20: Hardware Implementations
There is no one “best” method
Tradeoffs between cost and speed
  Design complexity matters, too
Standard cells are getting more expensive…
FPGAs are getting faster and bigger…
  This will affect future design choices
  For a given design, current best choice may not == future best choice!
Another choice to implement your digital design might be a programmable mController with off the shelf support hardware

## Slide 21: Tech Mapping: Std. Cells
Example boolean equation:
  z = a b c + c d + e
Example cell library:
  2-input NAND, INV
a
c
b
e
c
d
z
Been there…Done that…
This is what we are doing with our designs when synthesizing to the 35nm tsmc library
Resulting Tech Mapped Circuit:

## Slide 22: Tech Mapping: FPGAs
Need to know building blocks of the FPGA
  LUT size (if uses LUTs)
  Any special resources (Multipliers, RAMs)
Tech mapping then implements your netlist in terms of those building blocks

## Slide 23: Tech Mapping: FPGAs
Example boolean equation:
  z = a b c + c d + e
Example basic block:
  4-input LUT
Resulting tech-mapped circuit:
a
c
b
e
c
d
z
LUT #1
LUT #2

## Slide 24: Tech Mapping: FPGAs
Example boolean equation:
  z = a b c + c d + e
Example basic block:
  4-input LUT
Resulting tech-mapped circuit:
a
c
b
e
c
d
z
LUT #1
LUT #2
a b c
y
y + c d + e

## Slide 25: Placement
Standard Cells:
  Choosing a row for each cell
  Choosing a location within the row for each cell
  Cost function based
  Minimize ratsnest (interconnection)
  CTS will have priority in placing clock buffers
FPGAs:
  Choosing which physical LUTs implement each netlist LUTs

## Slide 26
Partitioning & Floorplanning (can be common to both StdCell and FPGA)
Sometimes you have BIG circuits
  Makes placement take a long time
  Yields poor results (too large a solution space)
Use partitioning and floorplanning
  Partitioning: Divide netlist into partitions
  Floorplanning: Assign partitions to chip regions
  Place regions separately
  Benefit: Small problems are easier to solve well than large ones
26

## Slide 27: Partitioning Example
27
A
B
C
D
E
G
F
H
I
J
K
L
How might we choose to form 3 partitions?

## Slide 28: Partitioning Example - Bad
A
B
C
D
E
G
F
H
I
J
K
L

## Slide 29: Partitioning
We want to try to make our partitions as independent as possible.
Independent = fewer outside connections
Why?
  Want to keep wires short
  Try to place partitions adjacent to the partitions they interconnect with
  If we have a lot of interconnections, this may not be easy/possible

## Slide 30: Partitioning Example - Bad
A
B
C
D
E
G
F
H
I
J
K
L

## Slide 31: Partitioning Example - Better
A
B
C
D
E
G
F
H
I
J
K
L

## Slide 32: Floorplanning
OK, so we’ve divided our problem up into partitions
Now, figure out where partitions should be placed relative to one another
Assign partitions to regions of the silicon / FPGA
Try to avoid long wires between partitions
Don’t want to have to route wires through too many other partitions
  Wastes area in those partitions
32

## Slide 33: Floorplanning Example
4
7
2
1
5
3
6
9
8

## Slide 34: Floorplanning Example
Try to arrange partitions to minimize cross-partition routing
4
7
2
1
5
3
6
9
8
Eat your heart out, Sudoku.

## Slide 35: Routing
Have locations for all the cells/LUTs in the netlist
Now need to connect them together to actually make the circuit
Different techniques for std. cell vs. FPGA
Divided into:
  Global
  Detailed (local)

## Slide 36: Global Routing
Find a rough path for each net
Figure out what areas a signal passes through

## Slide 37: Detailed Routing: Std. Cells
Connect the cells within the global regions
Goal: minimize channel width
Channel Width
1 2 2 4 4 0 3 0 4
2 4 4 3 0 0 3 3 1

## Slide 38: Detailed Routing: FPGAs
Assign signals in netlist to:
  Wires
  Switchbox points
Fixed set of available resources
  Can’t “widen” routing channels
Goal: Reduce congestion
  Congestion is the ratio of signals:wires
  By keeping areas “open”, more likely to be able to route later signals

## Slide 39: Detailed Routing: FPGAs
Goal: Reduce congestion

## Slide 40: Detailed Routing: FPGAs
Goal: Reduce congestion

## Slide 41: Detailed Routing: FPGAs
Frequently start with an “idealized” routing
  Signals can share wires
Repeatedly “rip up” and reroute
  One or more nets (signals)
Stop when no wires are shared

## Slide 42: Conclusion
Synthesis isn’t the end of the process!
  Many steps after it
Choose target implementation
  Examine cost/performance tradeoffs
Use CAD tools to implement synthesized circuit on FPGA or std. cells
  Place & Route
  Generate bitstream or layout masks
See ECE556 for more details on CAD algorithms